## Slide 1: At-Home Neurofeedback 05/17 – 06/08

## Slide 2: Dates of Neurofeedback Sessions:
Sunday | Monday | Tuesday | Wednesday | Thursday | Friday | Saturday
 |  | T, 5/17 | W, 5/18 | R, 5/19 | F, 5/20 | 
 | M, 5/23 | T, 5/24 |  |  |  | 
 | M, 5/30 |  |  |  |  | 
 |  |  | W, 6/8 |  |  | 
Recording Details:
E10 – E11
BW: 2.5
Center Frequency: 12.5 Hz
Gain: 4000
Stim ON
Tasks:
Motor task: Movement from one target to another target after a tone
Neurofeedback only
Neurofeedback plus movement task: NF to top or bottom target, then 3x taps between targets

## Slide 3: Ipsi Finger Movement Contra Finger Movement
Red is when tone is played, Green is power channel over M1, Spectrogram computed w/ pwelch

## Slide 4: Neurofeedback w/ Tapping Task:
Fixed decoder: Beta power mean = 375, std = 75 (from Power channel)
Decoding:
  Z-score current estimate of power (w/ mean and std)
  Transform zscore to the y-axis of the screen (-8, 8)
  Constant positional assist of 15%
NF Targets
  Only TOP and BOTTOM target
Tapping:
  Wearing glove w/ accelerometer
  Must tap between targets 3 x to complete the trial (cap touch sensors detect when target has been selected)

## Slide 5: Questions:
1. Does he learn?
  Over days?
  Within session?
2. What’s the effect of the week-long break in practice ?
3. Discernable effect of neurofeedback on following movement?
4. Mean beta trends with medication time or time of day?
5. How reliable is the setup?
  Dropped packets throughout session?
6. Future Improvements

## Slide 6: Presentation Notes
1. Colormap
  TOP target is Yellow
  BOTTOM target is Teal
2. ‘Consecutive’ Learning Data from Highlighted Days:
3. Neurofeedback = NF
S | M | T | W | R | F | S
 |  | T, 5/17 | W, 5/18 | R, 5/19 | F, 5/20 | 
 | M, 5/23 | T, 5/24 |  |  |  | 
 | M, 5/30 |  |  |  |  | 
 |  |  | W, 6/8 |  |  | 

## Slide 7: NF Learning Over Consecutive days

## Slide 8: NF Learning Within Consecutive days

## Slide 9: Adding Days with 1 week break: - Top Target is harder after 1 week break - Even middle target becomes harder
1 week
1 week
Weekend

## Slide 10: Is the 1 week break really a result of (un)learning, or can it be explained by a shift in baseline beta?
1 week
1 week
Reduction in
Baseline beta
Percent Correct (% of Targets Achieved / Total Targets presented in 5 min window)
Slight increase in
Baseline beta

## Slide 11: Questions:
1. Does he learn?
  Over days?
  Within session?
2. What’s the effect of the week-long break in practice ?
3. Discernable effect of neurofeedback on following movement?
4. Mean beta trends with medication time or time of day?
5. How reliable is the setup?
  Dropped packets throughout session?
6. Future Improvements

## Slide 12: Questions:
1. Does he learn?
  Over days?
  Within session?
2. What’s the effect of the week-long break in practice ?
3. Discernable effect of neurofeedback on following movement?
4. Mean beta trends with medication time or time of day?
5. How reliable is the setup?
  Dropped packets throughout session?
6. Future Improvements

## Slide 13: Kinematics from Tapping:
Total Tapping Time:
Reaction Time (Time to start first tap):

## Slide 14: Reaction Time from Touch Sensor is Best modeled as discrete groups:
RT From Task | Number of Trials | Percent low | P (not from fair coin), Binomial Test
1.2 – 1.6 sec | 14 | 57% low | P = 0.791
0.9 – 1.2 sec | 33 | 45% low | P = 0.728
0.5 – 0.9 sec | 89 | 41% low | P = 0.1374
0.1 – 0.5 sec | 48 | 29% low | P = 0.0055
HIGH targets appear to be faster

## Slide 15: Difficulty of Beta Task explains differences in Reaction Time?
Indeed, harder NF targets (evidenced by longer time to finish NF target, axis) are associated with a longer RT (slope of linear regression sig. > 0)
4 Consecutive Days had harder low beta target (see slide 10) possibly explaining the faster RTs for higher target

## Slide 16: Is there a trend in tapping times ? If so, we could potentially exclude early data when he is less proficient at tapping

## Slide 17: Questions:
1. Does he learn?
  Over days?
  Within session?
2. What’s the effect of the week-long break in practice ?
3. Discernable effect of neurofeedback on following movement?
4. Mean beta trends with medication time or time of day?
5. How reliable is the setup?
  Dropped packets throughout session?
6. Future Improvements

## Slide 18: Questions:
1. Does he learn?
  Over days?
  Within session?
2. What’s the effect of the week-long break in practice ?
3. Discernable effect of neurofeedback on following movement?
4. Mean beta trends with medication time or time of day?
5. How reliable is the setup?
  Dropped packets throughout session?
6. Future Improvements

## Slide 19
Beta power as function of:
Time of Day
Time Since last Med Dose

## Slide 20: Questions:
1. Does he learn?
  Over days?
  Within session?
2. What’s the effect of the week-long break in practice ?
3. Discernable effect of neurofeedback on following movement?
4. Mean beta trends with medication time or time of day?
5. How reliable is the setup?
  Dropped packets throughout session?
6. Future Improvements

## Slide 21: Questions:
1. Does he learn?
  Over days?
  Within session?
2. What’s the effect of the week-long break in practice ?
3. Discernable effect of neurofeedback on following movement?
4. Mean beta trends with medication time or time of day?
5. How reliable is the setup?
  Dropped packets throughout session?
6. Future Improvements

## Slide 22: Future Improvements to System:
Engineering
  Place Arduino on board instead of glove (heavy)
  Add a way to secure tapping pad to table
  Don’t use BT w/ Matlab (slow), just use serial connection for faster Fs and better power supply (USB port instead of batteries)
  Better sleeve for holding Nexus – Velcro sleeve instead of strap + clamps
  File writing mid-task (hdf files) instead of saving at end (and graceful failures) for data loss minimization
  Push buttons on board instead of touch sensors (make easier to push buttons)

## Slide 23: Future Improvements to System:
Patient Directions
  No movement
  Consistent strategy
Experiment Design
  Stream STN beta power channel (no additional battery drain)
  Reset decoder according to baseline @ beginning of each day
  Auto-adjust assist level (when getting better, make task harder slowly) ?

## Slide 24: Example Patient Strategies: Videos
1) Moving
2) ‘Piano playing’
3) ~Sleeping
4) Focusing
https://berkeley.app.box.com/files/0/f/8011975297/1/f_67419777141
https://berkeley.app.box.com/files/0/f/8011975297/1/f_66396078701

## Slide 25: Conclusions
Possible learning
Variable beta levels day-to-day that require daily recalibration
Many engineering fixes to the current system for heavier use
Better patient instructions are needed