## Slide 1: At Home BMI Summary
Preeya Khanna

## Slide 2: Overview:
10 Days:
  Thurs-Fri (2)
  Mon – Fri (5)
  Mon – Wed (3)
Different times of day
Daily metrics:
  A) Movement related desynchronization
  B) M1/STN Beta
  C) Left hand accelerometer sensors / pulse sensor
  D) Right hand IMU
  E) Mood assessments before/after training

## Slide 3: Task:
Get Cursor
to Center:
Cursor
in Center:
Get Cursor
to Periph:
TAP!
Cursor
in Periph:
Begin Finger-
tapping
Get Cursor
to Center:
Tap for
6 seconds
Details:
Periph target timeout = 60 seconds
Reward sound after tapping

## Slide 4: Decoder:
Calibrated from instructed delay task:
Calculate M1 mean/spread
Decoder is position decoder w/ smoothing (2 timesteps)
  Occasionally add assist if performance is poor

## Slide 5: Time to Top and Bottom Targets:

## Slide 6: Beta Modulation to Top / Bottom Targets:

## Slide 7: Beta Modulation to Top / Bottom Targets:

## Slide 8: How Different is Beta during Low / High Target?
M1 Beta Power Distributions for
High vs. Low Beta Target

## Slide 9: What About STN: Unlocks M1?
Background:
M1 leads STN in Beta oscillations
Apparent paradox: Levodopa therapy reduces beta power in STN but does not change power in M1
  dopamine suppresses transmission of hyper-synchronous cortical events to the STN–globus pallidus network
  Beta frequencies: M1 movement related beta is usually higher than levodopa-related beta reduction
Variable STN beta power reflects a cortico-thalamo-basal ganglia system that is less hyper synchronized
Weak correlation with M1 beta desynchronization
Notes: 5 min blocks
Cortical beta drives subcortical beta – resulting in hyper synchronization between these two.
Complicated – motor beta related to movement is in upper beta whereas levodopa reduces LOW beta in STN
Levodopa has not been conclusively shown to reduce cortico-STN coherence in the upper b frequency band
STN gamma LEADS motor cortex gamma (unlike beta)
Drop in STN beta correlates w/ RTs – STN beta must be desynchronized
  Paradox: How can cortical beta stay the same but STN beta increase so much if Ctx drives STN?
    Striatum does it (bc no dopa)
    Plasticity changes => oscillatory amplification
    STN/GPe interactions promote more beta
    Imbalance in hyperdirect and direct pathway

## Slide 10: Tapping Metrics?
Metric | High vs. Low Target
Movement Onset Time | Low target faster MOT
Spectral Peak Power | Low target more power
Spectral Peak | Low target faster
RMS Angle | Low target higher
RMS Angular Velocity | Low target higher
# Discrete Taps | More for lower target
TODO:
  Assess LH movement w/ tapping
  Split by Open vs. closed first

## Slide 11: Other Metrics
Mood (self-reported)
TODO:
  HR
Before NF
After NF