## Slide 1: At-home Neurofeedback
Update with 5 days

## Slide 2: Setup:
Daily:
  Arm movement task to assess mean and distribution of motor cortical beta power
  Fit beta to cursor mapping each day, based on the arm movement task
  Neurofeedback task with tapping after each trail
Neural Recording:
  Streaming M1 beta power channel (controls Neurofeedback cursor)
  Streaming STN beta power channel
Other Sensor:
  IMU on tapping hand
  Touch sensor on tapping hand
  Accelerometer on non-tapping hand
  Pulse sensor on non-tapping hand

## Slide 3: Neurofeedback Performance: Time to Target
Timeouts
Day 1
Day 2
Day 3
Day 4
Day 5
Low Target
High Target

## Slide 4: Beta Power Leading Up To Target Acquisition
High Target
Low Target
Day 1
Day 2
Day 3
Day 4
Day 5
Comments:
More beta increase and decrease to acquire targets than on day 1
Separation in high/low beta power earlier before target acquisition

## Slide 5: Distribution of Beta Power 5 seconds Prior to High / Low Targets
Histograms of beta power channel activity 5 sec preceding high/low beta target, aggregated for each day
Vertical bars indicate median of distribution
Oddly, in first few days, low target distribution had a higher median than high target distribution – maybe her strategy for the low target involved a synchronization followed by desynchronization ?

## Slide 6: Distribution of Beta Power 5 seconds Prior to High / Low Targets
From previous plot, if break up distributions into 10 min blocks and compute :
Median (High) – Median (Low)
See improvement over the five days
Getting better at separating her distributions from one another

## Slide 7: Observations
Baseline shifts in M1